***************************************************
GSM/GPRS/GPS Shield of Futura/Open-electronics

http://www.open-electronics.org/

http://store.open-electronics.org/index.php?route=common/home

***************************************************

***************************************************
For support use the issues' page on google code:

http://code.google.com/p/gsm-shield-arduino/issues/

or Arduino Forum

***************************************************

***************************************************
Library created by:

Marco Martines

martines[ dot ]marco[ at ]gmail[ dot ]com
***************************************************

[1]	How to switch between Arduino Mega and Arduino Uno?

1)
Open GSM.h and comment-decomment the appropriate lines like below
e.g. for Arduino Mega
//#define UNO
#define MEGA

2)
If you use Arduino Uno comment the line in HWSerial.h or decomment if
you are using Arduino Mega
e.g. for Arduino Mega
#define MEGA

3)
Save and compile

[2]	How to switch between the old shield (that uses 4 and 5 pins for
SoftwareSerial and the new (that used 2 and 3 pins)?

1)
Open GSM.cpp and comment-decomment the appropriate lines like below
e.g. for the new one

//#define _GSM_TXPIN_ 4
//#define _GSM_RXPIN_ 5
#define _GSM_TXPIN_ 2
#define _GSM_RXPIN_ 3

2)
Save and compile

[3]	My shield doesn't work. Why?

Check this steps and then ask for support on the issues' page on google
code.

1)	SIM900 and SIM908 require about 1 A during the hardest tasks.
You should have an external power source that can provide about
1 A at 8-12 V

2)	If the SIM90X blinks (1 Hz) for some seconds and then turn off,
probably it's a communication's problem. Check the switch/jumpers
for Serial communication.

3)	Arduino Uno has 2 KB of RAM. Library takes about 80% (we are working
to reduce it), if you use more than 20% left, Arduino can restart
or print on serial strange strings.